## Slide 2
ASSESSING THE IMPACT OF OFFSHORE WINDFARMS & CLIMATE CHANGE ON THE OCEAN & BIOGEOCHEMICAL STATE OF THE NORTH SEA
M. De Dominicis1, R. O’Hara Murray2, A. Gallego2, J. Jardine1, W. MacDonald2, M. Palmer3, T. Smyth3, J. Wihsgott3, C. Williams1, A. Zampollo2,4 & B. Scott4
(1) National Oceanography Centre
(2) Scottish Government Marine Directorate
(3) Plymouth Marine Laboratory
(4) University of Aberdeen
PELAgIO

## Slide 3: Shelf Sea Setting
Simpson and Sharples (2012)
Stratification
Shelf seas cover 7% of the ocean
Up to 30% of productivity at the bottom of the food chain
PELAgIO
Notes: To date wind farms have been installed in permanently mixed regions on monopiles or jacket foundations. The next phase of offshore wind development will be in deeper waters that undergo periodic or seasonal stratification, and floating foundations are likely to be used.

## Slide 4: Offshore wind farms could change mixing
Notes: Offshore wind development is now in deeper waters on the continental shelf (e.g. ScotWind and INTOG). Up to now they’ve mainly been deployed in shallower waters, closer to shore, and in well mixed areas. Deeper areas are likely to be seasonally stratified and floating foundations are likely to be used.
These figures are from a recent paper that suggests offshore wind infrastructure is likely to enhance mixing such that in crucial areas, such as front and stratified regions, the timing, strength and extent of stratification could change. This effect would also likely depend on the type of foundations being used.

## Slide 5: Mixing controls stratification
Wind farms can change mixing:
  Structures
  Wind speed deficit / acceleration
Stratification occurs intermittently and seasonally
Extent, location and timing of stratification could change
This could lead to changes in nutrient pathways and ecosystem functioning
Changing behaviours of fish and predators
Modified or redistributed mixing due to changes in wind speeds
PELAgIO
Notes: So, offshore wind farms could change mixing but Mixing controls stratification. There are two broad mechanisms for changing vertical mixing in the water column: structures and the associated drag and turbulence and changes in the wind field

## Slide 6: PELAgIO: WP1 fieldwork 2023 and 2024
PELAgIO
Notes: Fieldwork conducted over two cruises in May and Sep 2023 with Gliders undulating up and down through the water column from late April

## Slide 7: WP1 local scales: Mooring observations 2023
Mooring | N29 turbine | M0 | M2 | M1
Distance to OWF | 50 m | ~ 500 m | ~ 1 km | ~ 3 km
Sensors | 500 kHz ADCP Active acoustics Bed Fluorometer & Turbidimeter | 500 kHz ADCP Active acoustics Bed Fluorometer & Turbidimeter | 300 kHz ADCP full depth temperature & salinity chain | 250 kHz ADCP Seabed temperature sensor
Deployment dates | 10 Aug – 10 Dec 2023 | 6 May – 15 Jun 2023 | 6 May – 19 Sep 2023 | 6 May – 19 Sep 2023
Local scale
Regional scale
PELAgIO

## Slide 8: WP1 local scales: Mooring observations 2024
Local scale
Regional scale
Mooring | M1 | M2 | M3 | M4 | M5
Distance to OWF | 500m (down tide) | 500 m (down wind) | Inside Farm | ~ 3 km | 10 km
Sensors | 500 kHz ADCP Active acoustics Bed Fluorometer & Turbidimeter | 500 kHz ADCP Active acoustics Bed Fluorometer & Turbidimeter | 300 kHz ADCP full depth temperature & salinity chain lost | 250 kHz ADCP Seabed temperature sensor | Sonardyne Origin 600 kHz ADCP
Deployment dates | 3 May to 25 Sept 2024 | 3 May to 25 Sept 2024 | ADCP: 3 May to 25 Sep | 3 May – 25 Sep 2024 | 3 May – 8 Oct ? 2024
PELAgIO

## Slide 9
Data QC and analysis is ongoing.
6th May – 19th September 2023
The T&S chain consisted of 13 temperature sensors
  Including 3 CTDs (temperature, salinity and pressure)
  5 m vertical spacing of sensors, sampling every min
A ship collision 3 days before recovery resulted in the loss of five sensors covering the top 25 m of the water column & collapse of the chain
Supplemented with Operational Sea Surface Temperature and Sea Ice Analysis (OSTIA) data
Preliminary analysis:
Site seasonally stratified a few days after deployment
Thermocline is mostly unresolved due to missing surface sensors
Rate of change of bottom mixed layer temperature changes significantly from August 2023 onwards
WP1 local scales: Temperature & Salinity mooring 2023
Juliane Wihsgott, PML
OSTIA SST data
PELAgIO
Notes: The different colours in the plot show temperature from 8 sensors at depths ranging from 25 to 60 m +OSTIA, and the legend refers to the average depths of these loggers during the deployment.

## Slide 10
Gliders completed 36 transects between waypoints over 3 months
Sampled over 7 spring and neap periods.
Deepening of mixed layer from surface with enhanced winds
Comparing to models to separate high natural variability from the effect of the wind farms
Data to validate models and study local to regional effect of OWF
WP1 regional/shelf scales: Glider observations 2023
Time (May to Aug)
Charlotte Williams, NOC
Notes: Gliders were implemented to provide an idea of spatial and temporal variability >10km from wind farm.
Two gliders measuring:
  'Churchill': temperature, salinity, depth, chlorophyll and dissolved oxygen.
  'Zephyr': temperature, salinity, depth, chlorophyll and dissolved oxygen and TKE dissipation rate.
  Top panel is temperature, second is showing the strength of stratification calculated from the density, third panel is chlorophyll concentration and bottom panel is dissolved oxygen. Enhanced chlorophyll shown at the density interface – enhanced oxygen shown here as well.
Results will be used to validate the model and quantify local to regional footprint of OWF.

## Slide 11
Interannual variability
Longitude
Pressure (dbar)
Example transect of temperature from W to E
WP1 short and medium term temporal scales 2023
No change in rate of warming in bottom water following the marine heatwave in June.
Charlotte Williams, NOC &
Juliane Wihsgott, PML
PELAgIO gliders sampled within a hotspot of the marine heatwave - sea surface temperatures > 4oC hotter than the seasonal average which classifies its severity as 'extreme' (Category 4).
Short term variability
Sea surface temperature ˚ C
Temperature ˚ C
May- August 2023
Near surface temperature
Near bed temperature
Depth
Temperature
Depth
Temperature
The marine heatwave causes a shoaling of the surface mixed layer and stronger thermal stratification which prevents mixing of heat, nutrients and dissolved gasses (O2) across the thermocline.
Marine Heatwave
Berthou et al., 2024
Notes: Top left plot: Transect from SG to eastern waypoint; Gliders took 1-1.5 days to complete one leg of transect. - evidence of short term and temporal variability
Marine heatwave plot: Sea surface temperature from gliders (blue Zephyr and yellow Churchill) are overlaid to OSTIA SST product interpolated onto glider location (grey). Black plot shows 1981-2010 climatology with 10th/90th percentile band shown as shading which marks the threshold for a heat/coldwave.
OSTIA SST climatology
Increased strat from marine heatwave, N2 higher, reduction of mixing form SML to BML.

## Slide 12: WP1: Modelling all Scales: Windfarm and Climate 3 SPATIAL SCALES
Local: idealized channel Regional: FVCOM+ERSEM Shelf Wide: FVCOM+ERSEM+Climate
(10 m-1 km) (1-100 km) (>1000 km)
Resolving all proposed east coast OWFs
High resolution nested Seagreen grid
PELAgIO
Notes: A local SeaGreen Model & idealized channel that has been implemented and used to test the sensitivity to resolution & parameterizations (including non-hydrostatic runs).
Simulated channel (similar to the flume experiments done in Cazenave et al 2016) to isolate the exact effect of parameterisation on mixing in the downstream water column, using dry cells and comparing with the drag & mixing parameterizations.
The wind-wake parameterization will also be improved to included individual wakes and wakes interactions.
The underwater structure and wind-wake parameterizations, after being validated against turbulence, mixing and current observations, will be used in the regional FoF and in the shelf-wide North-West European Shelf FVCOM-ERSEM model runs.
Use of Field Data for Large-Scale
Estimates of depth resolved PP from gliders derived from chl-a, O2 measurements local to regional scales, including temporal and spatial variability and physical effects of OWF.
Underwater structure drag to be accurately parameterized (which has been implemented into FVCOM and the k-epsilon scheme in GOTM has been modified to include dissipation/ mixing due to underwater structure).

## Slide 13: 2 OWF MODEL PARAMETERISATIONS to include both mechanisms through which an OWF can change the mixing and stratification
structure drag and mixing effects of the underwater structure: induced drag generated by the underwater structures and consequent induced mixing in the wake of the OWF
modified wind field to reproduce the ‘wind wake effect’: wind speed reduction in the wake of the OWF when it is operating
Modified from Shaw et al 2022
The 2023 and 2024 fieldwork data taken in the vicinity of Seagreen are being used to calibrate the drag and turbulence, and wind-wake OWFs parameterisations in models.
PELAgIO

## Slide 14: 3 MODELS: HYDRODYNAMIC-TURBULENCE-BIOGEOCHEMISTRY
Modified from Ciavatta et al 2011
FVCOM & GOTM
T, S,
u,v,w,k
Primary productivity
Dissolved oxygen
ChL-a
ERSEM
Modified from Butenschön et al 2016
PELAgIO

## Slide 15
Wind-wake effects on biogeochemistry
Arianna Zampollo, UoA
Rory O'Hara Murray, MD
Chl-a MAX
PELAgIO
Notes: Michela and I have previously represented tidal turbine structures as a momentum sink, and we’re now using this again to represent the wind turbine structures. Just changing the drag coefficient and the cross-sectional area of the structures appropriately.
Michela has also recently now followed the approach of Rennau et al and additional terms to GOTM to represent the structure-induced friction, addition TKE production and rate of dissipation.
Michela and I have both now implemented this in our models and find that the changes to TKE lead to an order of magnitude greater change than just the momentum sink. This is the changes in mixing that I’ve outlined previously.
ROM:
Models sensitive to parameter values. Sensitivity analysis using high res model and observations
Above water impact (wind field changes)

## Slide 16
GLIDERS
MOORINGS
CTD
Effects of structures drag & mixing
SUMMER seasonal changes – Potential Energy Anomaly
Michela De Dominicis, NOC
PELAgIO

## Slide 17: Temperature comparison with 2023 observations
Effects of structures drag & mixing
Rory O'Hara Murray, MD
PELAgIO
MAY 2023
JUNE 2023

## Slide 18
  Climate change
  STRATIFICATION (PEA)
  Present climate
  STRATIFICATION (PEA)
  Change due
  to offshore wind structures
  (work in progress, PELAgIO)
We need multi-year model simulations with/without OWFs to disentangle natural variability (and climate change) from OWFs induced changes.
  NATURAL VARIABILITY
  (work in progress, PELAgIO)
Shelf scale OWF changes vs climate change
Michela De Dominicis, NOC
Jenny Jardine, NOC
PELAgIO
Notes: Negative NOA in 2010 (unusual)
Do winfarm mitigate/etc effects of NAO?
List ersem parameters jenny's including.
RCP8.5 but maybe other ssp scenarios are ready?
How far into the future? and how many wind farms?
Wind sceanrios - practical work putting dots on a map.
One WF scenario for JJ
Arianna to do 2-3 I think.

## Slide 19
2010-2012
FVCOM-ERSEM ​
2050 RCP8.5 FVCOM-ERSEM
WITH/WITHOUT 2050 OWFs
REGIONAL & SHELF WIDE OUTPUTS
UNDER CONSTRUCTION
2008-2017
FVCOM-ERSEM
UNDER CONSTRUCTION
2008-2017 FVCOM-ERSEM WITH OWFs
PELAgIO

## Slide 21: Sampling challenges in offshore windfarms generate innovation in marine autonomous systems
Josh Lawrence & Paul Fernandes

## Slide 22
Seabed
Traditional vessels:
Large
  Navigational constraints
Risky:
  Personnel
  Infrastructure
  Other vessels
Expensive
Large carbon footprint
ECOWINGS goal: understand cumulative impacts of OWFs on seabirds and the wider ecosystem
This work:
Aims to quantify fish distributions in and around OWFs
Relate fish data to seabird distributions
But how?
The scientific echosounder

## Slide 23
USV
AUV
Innovative sampling and modelling of the distribution of seabirds and their prey
USV
Aeroplane
Alternative platforms will overcome these challenges
USV
Small
Safe
Low carbon
Cheap(er)
Acoustic view?
AUV
Unsampled

## Slide 24
Innovation required for surveying OWFs: USV
Survey requirements:
‘Long’ range
Communications
Echosounder
Started from ‘bare bones’ vessel:
Floated(!)
Battery only
One camera
Limited comms
No echosounder
2 years ago…
Now:
Still floats
Battery + diesel generator
360° cameras
Over the horizon comms
  Starlink
  + backup systems
Echosounder
  Drop-keel for data quality
6 weeks ago…
20 nmi

## Slide 25
400
1200
2000
2800
Distance (m)
0
75
25
50
USV Data
Depth (m)
Recent developments and plans
Sea trials October 2024
USV @ Millport
First data collection with newly fitted echosounder
  High quality data
All communications & control systems operational
Echo
strength
High
Low
Fish schools
Seabed

## Slide 26
Recent developments and plans
Sea trials October 2024
USV @ Millport
First data collection with newly fitted echosounder
  High quality data
All communications & control systems operational
Future plans:
Additional USV developments:
  VHF
  Fuel tank
Survey preparation over winter
  MCA certification
  Liaise with OWF operators
Data collection from April 2025 onwards
Any questions?
(Also see poster!)

## Slide 27: Assessment of impacts associated with electromagnetic fields produced by HV submarine cables
Joanna Rzempołuch1, George Callender1, Justin Dix2, Martin Solan2, Jasmin Godbold2, Oscar Ward3, Liesl van der Blackman2, Liam Ferdinand3, Kevin Goddard1, Sunny Chaudhary1, Paul Lewin1, and Huw Powell1
20th of November 2024
email: jr9g20@soton.ac.uk
1Tony Davies High Voltage Laboratory, University of Southampton, Southampton, United Kingdom
2Ocean and Earth Sciences, University of Southampton, Southampton, United Kingdom
3ERM Limited, Norwich

## Slide 28: Research Problem
Offshore infrastructure
Marine animals
Question: Is the increasingly present infrastructure impacting the marine life?

## Slide 29: Overview
Research Problem
Modelling of EMFs Produced by HV Subsea Cables (Poster 1)
Meta-analysis of the impacts of EMF on marine ecosystems: what do we actually know? (Poster 2)
SCAMPI (Synthetic Cable for the Assessment of Marine Power Impacts) (Poster 3)

## Slide 30: Poster 1: Modelling of EMFs produced by HV submarine cables
Problems with existing approaches for EMFs calculation:
complexity, universality, computational cost, accessibility
Numerical approaches:
accuracy, complexity, accessibility
Analytical approaches:

## Slide 31: Poster 1: Modelling of EMFs produced by HV submarine cables
Implementation of analytical solutions of varying complexity through MATLAB/Python code validated by numerical solutions
Aim: Calculation of EMFs from different subsea cable systems at low computational cost, in an accessible way with a good level of accuracy.

## Slide 32: Poster 2: Meta-analysis
2 m
0.5 m
AC Cable Surface
26+ experiments
No Effect
Positive Effect
Negative Effect
1 m
Meta-analysis review suggests from 26+ experiments that there are no demonstrable effects until within 0.5 m of high load cable and realistically not until existing on the cable surface.
Factors analysed include an assessment of the magnetic and electric field strengths, duration of exposure, nature of source (AC vs DC) and the species type and life stage.
The fields used in literature have been compared with data derived from physics-based models (Poster 1) and with full consideration of the installation and operating conditions.
These insights have been used to inform a new set of experiments to be undertaken as part of (SCAMPI: Poster 3).
AC

## Slide 33: Poster 3: SCAMPI (Synthetic Cable for the Assessment of Marine Power Impacts
Modelling and Design
Testing
+Other Considerations
Aim: Design of a device that recreates the EMFs created by HV submarine cable systems (i.e. the magnitude, distribution and orientation of the fields) that can be used for marine biology experiments.

## Slide 35: Quantifying the impact of offshore wind farm infrastructure using Earth Observation
Tim Smyth, Juliane Wihsgott, Dan Clewley, Silvia Pardo, NEODAAS
PELAgIO

## Slide 36: What are we looking for?
“Smoking gun” of evidence that offshore wind infrastructure disrupts the marine ecosystem
Dorrell et al., (2022)
PELAgIO

## Slide 37: Evidence investigation #1
Ocean Colour (chlorophyll)
Anomaly plots vs 1998 – 2020 climatology
Verdict
Spatial resolution too coarse
Temporal resolution too coarse
Coverage too patchy
Natural spatio-temporal variability too high
PELAgIO

## Slide 38
Sea Surface Temperature (SST)
Anomaly plots vs 1991 – 2020 climatology
Verdict
Spatial resolution too coarse
Temporal resolution too coarse
Coverage too patchy
Natural spatio-temporal variability too high
Evidence investigation #2
PELAgIO

## Slide 39
Evidence investigation #3
Synthetic Aperture Radar (SAR)
Do we trust SAR to give accurate wind retrievals? YES
PELAgIO

## Slide 40
Evidence investigation #3
Synthetic Aperture Radar (SAR)
PELAgIO
What do the data look like?
  Evidence for both deceleration and acceleration behind turbines
28/08/2023
11/09/2023

## Slide 41
Evidence investigation #3
Synthetic Aperture Radar (SAR)
PELAgIO
Both deceleration and acceleration observed previously
  Function of atmospheric stability (Hasager et al., 2024)

## Slide 42
Evidence investigation #3
Synthetic Aperture Radar (SAR)
PELAgIO
Quantifying impact: relative wind speed relative to upwind reference
Turbine location
Turbine operating

## Slide 43
Evidence investigation #3
Synthetic Aperture Radar (SAR)
PELAgIO
Quantifying impact: is deficit linked to turbine operation?

## Slide 44
Evidence investigation #3
Synthetic Aperture Radar (SAR)
PELAgIO
Quantifying impact: Looking at convergence / divergence patterns
Divergence
Speed up
Convergence
Slow down

## Slide 45
Have we found what we’re looking for?
“Smoking gun” of evidence that offshore wind infrastructure disrupts the marine ecosystem
  Not directly, but evidence that we can further use to quantify impacts on wind driven upwelling
Dorrell et al., (2022)
PELAgIO